## Slide 1
INFOSYS SPRINGBOARD PROJECT
AI-Based Industrial Maintenance and Process Optimization for Smart Manufacturing
TEAM MEMBERS
TP
Thamma Pavani
NN
Natakarini Nirupa
NK
Neelima Kesanakurthi
ND
Nagaroopini D
PH
Priyanka H C
M
Mahesh
Team abbreviations used as member IDs in the available project material.

## Slide 2
PROJECT OVERVIEW
2
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
From Machine Data to Predictive Action
The system transforms historical machine readings into failure-risk insights and operator-facing recommendations.
D
DATA
AI4I 2020 dataset
P
PREP
Clean + encode + scale
T
TRAIN
Compare 3 classifiers
P
PREDICT
Failure-risk probability
V
VISUALIZE
Fleet + process analytics
A
ASSIST
Groq AI maintenance chat
PROJECT SCENARIO: 10-MACHINE FLEET
WITHOUT PREDICTION
Failure happens before maintenance is planned.
Downtime becomes a production problem.
WITH THE SYSTEM
Risk is surfaced before the machine becomes critical.
Maintenance attention can be prioritized.

## Slide 3
PROBLEM & OBJECTIVES
3
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
The problem is not only failure — it is delayed visibility
The project focuses on making machine health easier to observe, predict and act on.
CORE PROBLEM
Maintenance teams may react after failure symptoms become severe.
Raw sensor readings are difficult to convert into a single risk view.
Different machines need different levels of maintenance attention.
Operators need explanations, not only model probabilities.
PROJECT OBJECTIVES
01
Predict
Estimate failure risk from machine conditions.
02
Monitor
Show fleet health and critical machines.
03
Analyze
Expose model and process-level insights.
04
Assist
Provide natural-language maintenance guidance.

## Slide 4
SYSTEM ARCHITECTURE
4
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
End-to-End Data Pipeline
A single workflow connects the dataset, preprocessing, machine learning, dashboard and AI assistant.
01
DATA
AI4I 2020 10,000 records
02
PREP
Encode + scale train/test split
03
MODEL
LR + RF + XGBoost compare accuracy
04
APP
Streamlit 5 functional areas
05
AI
Groq + Llama 3.3 maintenance chat
OUTPUT: MACHINE HEALTH • FAILURE RISK • PROCESS TRENDS • MAINTENANCE GUIDANCE

## Slide 5
DATA FOUNDATION
5
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
AI4I 2020: The Data Foundation
The implementation uses the public predictive-maintenance dataset as the model-training source.
10,000
records
14
original columns
339
failure cases
80 / 20
train / test
KEY INPUT FEATURES
Air temperature Process temperature Rotational speed • Torque • Tool wear
TARGET + PREPARATION
Target: Machine failure Type encoded as L=0, M=1, H=2 StandardScaler → model-ready features

## Slide 6
DATA PREPARATION
6
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
Preparing the Data for Reliable Inference
The same feature transformation used during training is reused when the dashboard loads the model.
D
DROP
UDI + Product ID
E
ENCODE
Machine Type
S
SPLIT
80% train / 20% test
S
SCALE
StandardScaler
S
SAVE
model.pkl + scaler.pkl
WHY THIS MATTERS
A deployed model must receive features in the same order and scale as training. The project persists both the trained model and scaler for reuse by the dashboard.

## Slide 7
MACHINE LEARNING
7
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
The ML Layer: Compare, Evaluate, Select
Three classifiers are trained on the same prepared feature set.
L
LOGISTIC REGRESSION
Linear classification baseline
TRAIN → TEST → COMPARE
R
RANDOM FOREST
100-tree ensemble model
TRAIN → TEST → COMPARE
X
XGBOOST
Gradient-boosted comparison model
TRAIN → TEST → COMPARE
MODEL SELECTION RULE: HIGHEST TEST ACCURACY → SAVE BEST MODEL → LOAD IN STREAMLIT

## Slide 8
MODEL RESULTS
8
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
Model Performance: Current Implementation
The training script reports 0.9990 test accuracy for each of the three classifiers.
TEST ACCURACY
99.9%
0.9990 on the current test split
ALL 3 MODELS: 0.999
COMPARISON
Logistic Regression
99.9%
Random Forest
99.9%
XGBoost
99.9%
Evaluation note: failure-mode flags can create leakage if they are only known after a failure. Production retraining should use genuinely pre-failure signals.

## Slide 9
DASHBOARD
9
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
A Live-Style Streamlit Interface
The application brings model results, fleet health, process trends and AI support into one place.
01
Dashboard & Digital Twin
Fleet risk cards
02
ML Model Performance
Metrics + feature importance
03
Process Intelligence
Trends + CSV upload
04
AI Assistant
Groq maintenance chat
05
About & Team
Project context
BUILT WITH STREAMLIT + PLOTLY

## Slide 10
PREDICTIVE MAINTENANCE
10
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
Digital Twin: Fleet Health at a Glance
The dashboard demonstrates a 10-machine fleet with model-driven risk classification.
M-01
HEALTHY
FAILURE RISK
18%
M-02
WARNING
FAILURE RISK
54%
M-03
CRITICAL
FAILURE RISK
86%
M-04
HEALTHY
FAILURE RISK
12%
M-05
WARNING
FAILURE RISK
41%
M-06
HEALTHY
FAILURE RISK
9%
STATUS LOGIC: HEALTHY < 30% • WARNING 30–70% • CRITICAL ≥ 70%

## Slide 11
PROCESS INTELLIGENCE
11
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
Process Intelligence: Turning Readings into Insight
The dashboard provides trend analysis, failure-type breakdowns and CSV-based investigation.
SENSOR TREND VIEW
temperature torque rotational speed
FAILURE-TYPE VIEW
TWF • HDF • PWF OSF • RNF
CSV ANALYSIS
Upload data → inspect columns → visualize trends → support investigation

## Slide 12
AI ASSISTANT
12
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
AI Maintenance Assistant
The Groq-powered assistant gives operators a natural-language way to ask about the fleet.
GROQ • LLAMA 3.3 70B VERSATILE
Which machine needs attention right now?
Prioritize the highest-risk machine, then inspect its operating conditions and recent trends before maintenance action.
Ask about machine health, risk or maintenance advice…
HOW IT WORKS
F
FLEET CONTEXT
Current dashboard state
U
USER QUERY
Natural-language question
G
GROQ API
LLM response generation
G
GUIDANCE
Maintenance-oriented answer

## Slide 13
TECHNOLOGY & SECURITY
13
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
Technology Stack, Security & Deployment
The implementation combines Python analytics, Streamlit, ML artifacts and secure API configuration.
P
Python
Core application language
p
pandas + scikit-learn
Data prep + ML
X
XGBoost
Gradient boosting
S
Streamlit + Plotly
Dashboard + charts
G
Groq / Llama 3.3 70B
AI assistant
j
joblib
Model persistence
SECURITY CONTROLS
Authenticated access • bcrypt password hashing • session state • GROQ_API_KEY stored in .env

## Slide 14
WHY IT MATTERS
14
AI-DRIVEN PREDICTIVE MAINTENANCE & PROCESS INTELLIGENCE
From Prediction to Maintenance Intelligence
The project demonstrates how machine learning, interactive analytics and generative AI can work together in a smart-manufacturing workflow.
M
Predict risk
D
Understand trends
D
See fleet health
A
Support decisions
S
Protect access
NEXT STEP FOR PRODUCTION
Retrain with only pre-failure signals • validate on real telemetry • connect maintenance work orders • harden deployment
Thank You
Questions & Discussion Welcome
Thamma Pavani • Natakarini Nirupa • Neelima Kesanakurthi • Nagaroopini D • Priyanka H C • Mahesh